===== Parallax PIC16Cxx Assembler v4.7 =====

1                              	;		IR REMOTE CONTROL

2                              	;	for Toshiba CATV Home Terminal model TCJ552B

3                              	;		Version 3.1

4                              	;	Copyright 2001 Tickets, All rights reserved

5                              	;

6                              	; * Use 3.58MHz resonator for proper operation

7                              	;

8                              	; NOTE: This code is written in Parallax SPASM assembler

9                              	;

10    0000-                     		device	pic16f84,hs_osc,wdt_off,protect_off,pwrt_on

11    0000-                     		ID	'IRRC'

12                              	;++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

13                              	; DEFINITIONS

14                              	;++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

15                              	; Version

16    =0033                     	ver_major	=	'3'	; Major version

17    =0031                     	ver_minor	=	'1'	; Minor Version

18

19                              	; IR LED

20    =0205                     	led_out		=	PortA.4	; LED output/Active Low

21

22    =0016                     	time_h		=	22	; Cycles of H bit for 0.56msec

23    =0078                     	time_0		=	120	; L duration for data 0

24    =00FA                     	time_1		=	250	; L duration for data 1

25    =005F                     	time_start	=	95	; Cycles of Leader (+255)

26

27    =005A                     	delay_repeat	=	90	; Adjust for 108msec interval

28    =0028                     	delay_gap	=	40	; Gap for first repeat code

29

30    =0008                     	bit_cnt		=	8	; Bit count

31

32                              	; Key scan

33    =0049                     	code_system	=	49h	; Toshiba

34    =001C                     	key_shift	=	1ch	; Key scan code of SHIFT

35    =000C                     	key_chup	=	0ch	;                  Channel Up

36    =0010                     	key_chdn	=	10h	;                  Channel Down

37    =0014                     	key_vrup	=	14h	;                  Volume Up

38    =0018                     	key_vrdn	=	18h	;                  Volume Down

39    =0020                     	data_shift	=	32	; Add to key code in shift mode

40    =0206                     	col0		=	PortB.4	; COLUMN scan ports (Input)

41    =0286                     	col1		=	PortB.5

42    =0306                     	col2		=	PortB.6

43    =0386                     	col3		=	PortB.7

44

45    =00FF                     	no_key		=	0ffh	; Key matrix code for no key

46

47                              	; Port Settings

48    =00E0                     	porta_dir	=	11100000b

49    =00F0                     	portb_dir	=	11110000b

50    =0010                     	porta_ini	=	00010000b

51    =0000                     	portb_ini	=	00000000b

52    =0381                     	portb_pullup	=	OPTION.7	; 0 to enable PortB pull-up

53

54                              	; Control registers settings

55    =0000                     	mask_int	=	00000000b	; INTCON register

56    =007F                     	mask_opt	=	01111111b	; OPTION register

57

58                              	; Interrupt

59    =000B                     	int_rbif	=	INTCON.0	; PortB interrupt flag

60    =010B                     	int_toif	=	INTCON.2	; WDT

61    =018B                     	int_rbie	=	INTCON.3	; PortB interrupt enable

62    =038B                     	int_gie		=	INTCON.7	; General interrupt enable

63

64                              	;++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

65    000C-                     		org	0ch	; Top of available RAM

66

67    000C-                     	time_cntr	ds	1	; Cycle counter

68    000D-                     	delay_cntr	ds	1	; Delay counter

69    000E-                     	cntr_1msec	ds	1	; Counter for 1msec wait

70    000F-                     	cntr_15msec	ds	1	; Counter for 16msec wait

71    0010-                     	cntr_100msec	ds	1	; Counter for 100msec wait

72    0011-                     	cntr_1sec	ds	1	; Counter for 1sec wait

73    0012-                     	cntr_nmsec	ds	1	; Counter for N msec wait (N in W)

74

75    0013-                     	tx_data_buff	ds	1	; Store code to be transmitted

76    0014-                     	code_buff	ds	1	; Store result data code from key_scan

77    0015-                     	bit_cntr	ds	1	; Bit counter to send byte

78

79    0016-                     	key_row		ds	1	; Row for keyscan

80    0017-                     	key_column	ds	1	; Column for keyscan

81    0018-                     	key_matrix	ds	1	; Result key matrix code (0-63)

82    0019-                     	cntr_row	ds	1	; Counter for row scan

83    001A-                     	cntr_col	ds	1	; Counter for column scan

84    001B-                     	cntr_nokey	ds	1	; Counts key scan cycles to sense no-key

85    001C-                     	shift_32	ds	1	; Contains 00100000b in shift mode

86    001D-                     	flag_row	ds	1	; NZ if row scan get key press

87    001E-                     	flag_col	ds	1	; NZ if column scan get key press

88    001F-                     	flag_nokey	ds	1	; NZ if no key is pressed for a while

89    0020-                     	flag_continue	ds	1	; NZ if key press is continued

90

91    0021-                     	flag_error	ds	1	; 0:No error  NZ:Error

92

93                              	;++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

94    0000-                     		org	0		; Top of program

95    0000- 280C                		jmp	start

96

97    0001-                     	interrupt_routine

98    0004-                     		org	04h		; Interrupt vector/NOT USED

99

100    0004- 0009                		reti			; End of interrupt

101                              	; Version number

102    0005- 3456 3465 3472 342E 		retw	'Ver.',ver_major,'.',ver_minor

0009- 3433 342E 3431

103

104                              	;-------------------------

105    000C-                     	start

106    000C- 205B                		call	init

107

108                              	;-------------------------

109                              	; MAIN LOOP

110                              	;-------------------------

111    000D-                     	main

112    000D- 3010 0085           		mov	PortA,#10h	; Set scan port output to L

113    000F- 3000 0086           		mov	PortB,#0h

114

115    0011- 0806                		mov	w,PortB		; Clear PortB input mismatch

116    0012- 100B                		clrb	int_rbif	; Clear RBIF for sure

117    0013- 158B                		setb	int_rbie	; Enable PortB mismatch int

118

119    0014- 0063                		sleep			; Sleep untill interrupt occurs

120                              					; Process next instruction on interrupt

121                              					;  No interrupt vector (04h) called

122                              					;  since GIE is disabled

123    0015- 118B                		clrb	int_rbie	; Disable PortB interrupt

124    0016- 100B                		clrb	int_rbif	; Clear PortB interrupt flag

125

126    0017- 2169                		call	delay_1msec	; Remove key bounces

127    0018- 206A                		call	process_key	; Main Process

128

129    0019- 280D                		goto	main		; Wait for next key

130

131                              	;--------------------------------------------

132                              	; KEY SCAN TABLE

133                              	; This should be placed within first 256 byte

134                              	;--------------------------------------------

135    001A-                     	key_table

136    001A- 0782                		jmp	pc+w			; W contains matrix code

137                              						; Returns data code in W

138                              						; 55h should be ignored

139    001B- 3412 3411 340F 3415 		retw	12h,11h,0fh,15h,16h,1ch,55h,1dh

001F- 3416 341C 3455 341D

140    0023- 3417 3400 3419 3414 		retw	17h,00h,19h,14h,1bh,03h,02h,01h

0027- 341B 3403 3402 3401

141    002B- 341F 3406 3405 3404 		retw	1fh,06h,05h,04h,1ah,09h,08h,07h

002F- 341A 3409 3408 3407

142    0033- 341E 3418 340B 340A 		retw	1eh,18h,0bh,0ah,55h,10h,13h,0eh

0037- 3455 3410 3413 340E

143

144    003B- 34FF 3455 3443 3455 		retw	0ffh,55h,43h,55h,55h,5dh,44h,4eh

003F- 3455 345D 3444 344E

145    0043- 3455 3455 3445 3455 		retw	55h,55h,45h,55h,55h,55h,5bh,55h

0047- 3455 3455 345B 3455

146    004B- 3455 3455 345C 3455 		retw	55h,55h,5ch,55h,42h,55h,5eh,55h

004F- 3442 3455 345E 3455

147    0053- 3455 3455 345F 3441 		retw	55h,55h,5fh,41h,55h,55h,0feh,40h

0057- 3455 3455 34FE 3440

148

149                              	;-------------------------

150                              	; POWER ON INITIALIZE

151                              	;-------------------------

152    005B-                     	init

153    005B- 3000 008B           		mov	INTCON,#mask_int

154    005D- 307F 0081           		mov	OPTION,#mask_opt

155    005F- 138B                		clrb	int_gie		; Disable GIE

156                              					; Ports Direction

157    0060- 30E0 0065           		mov	!ra,#porta_dir	; All PortA for output

158    0062- 30F0 0066           		mov	!rb,#portb_dir	; RB0-3 for output, RB4-7 for output

159    0064- 3010 0085           		mov	PortA,#porta_ini	; row4-7 to L,led_out to H

160    0066- 3000 0086           		mov	PortB,#portb_ini	; row0-3 to L

161

162    0068- 019C                		clr	shift_32	; Clear shift data (32)

163

164    0069- 0008                		ret

165

166                              	;-------------------------

167                              	; Process Key Input

168                              	;-------------------------

169    006A-                     	process_key

170    006A- 01A0                		clr	flag_continue	; Prepare for new key input

171    006B-                     	:loop

172    006B- 20A5                		call	key_scan	; Scan keys

173

174    006C- 30FF 0218 1903 28A2 		cje	key_matrix,#no_key,:finish	; No key, do nothing

175

176    0070- 3000 0220 1903 288C 		cje	flag_continue,#0,:skip0		; Skip0 if not continue

177    0074- 300C 0218 1903 2886 		cje	key_matrix,#key_chup,:skip3	; Repeat Channel Up

178    0078- 3010 0218 1903 2886 		cje	key_matrix,#key_chdn,:skip3	; Repeat Channel Down

179    007C- 3014 0218 1903 2886 		cje	key_matrix,#key_vrup,:skip3	; Repeat Volume Up

180    0080- 3018 0218 1903 2886 		cje	key_matrix,#key_vrdn,:skip3	; Repeat Volume Down

181

182    0084- 2162                		call	delay_15msec			; Eliminate key bounce

183    0085- 289F                		goto	:skip2				; Don't process

184

185    0086-                     	:skip3					; Send Repeat code

186    0086- 20FE                		call	tx_leader		; 9.0msec leader

187    0087- 2168                		call	delay_2msec		; 2.25msec gap

188    0088- 2138                		call	tx_bit			; 0.56msec 1

189    0089- 305A                		mov	w,#delay_repeat		; 108msec interval

190    008A- 2157                		call	delay_nmsec

191    008B- 289F                		goto	:skip2

192

193    008C-                     	:skip0

194    008C- 301C 0218 1D03 2898 		cjne	key_matrix,#key_shift,:skip	; Skip if not shift

195    0090-                     	:wait_release

196    0090- 20A5                		call	key_scan	; Wait till SHIFT key is released

197    0091- 301C 0218 1903 2890 		cje	key_matrix,#key_shift,:wait_release

198

199    0095- 3020 009C           		mov	shift_32,#data_shift

200    0097- 28A2                		goto	:finish		; Shift data is set

201

202    0098-                     	:skip				; Normal transmission process

203    0098- 0818                		mov	w,key_matrix	; Set key matrix code

204    0099- 201A                		call	key_table	; Get Remote Control code

205    009A- 0094                		mov	code_buff,w	; Set in transmit buffer

206

207    009B- 20E9                		call	tx_data		; Send IR

208

209    009C- 019C                		clr	shift_32	; Reset shift mode

210

211    009D- 3028                		mov	w,#delay_gap

212    009E- 2157                		call	delay_nmsec	; Adjust gap before repeat code

213    009F-                     	:skip2

214    009F- 3001 00A0           		mov	flag_continue,#1	; Set continue flag

215    00A1- 286B                		goto	:loop

216

217    00A2-                     	:finish

218    00A2- 01A0                		clr	flag_continue	; Key released

219    00A3- 2162                		call	delay_15msec	; Eliminate key bounce

220

221    00A4- 0008                		ret

222

223                              	;-------------------------

224                              	; KEY SCAN

225                              	;-------------------------

226    00A5-                     	key_scan

227    00A5- 0198                		clr	key_matrix	; Initialize scan matrix

228

229    00A6-                     	:loop1

230    00A6- 0197                		clr	key_column	; Prepare for new scan

231    00A7- 301F 0085           		mov	PortA,#1fh	; Clear PortA

232    00A9- 30FE 0086           		mov	PortB,#0feh	; Set RB0 to low

233    00AB- 3004 009A           		mov	cntr_col,#4	; Test four times

234    00AD-                     	:loop2

235    00AD- 20D8                		call	row_scan

236    00AE- 3000 049D           		or	flag_row,#00h	; Test flag

237    00B0- 1D03 28CC           		jnz	:finish		; Yes, key is pressed

238

239    00B2- 1403                		setb	c		;

240    00B3- 0D86                		rl	PortB		; Next row

241    00B4- 0A97                		inc	key_column	; Increment Key Matrix code

242

243    00B5- 0B9A 28AD           		djnz	cntr_col,:loop2

244

245    00B7-                     	:loop3

246    00B7- 301E 0085           		mov	PortA,#1eh	; Set RA0 to low

247    00B9- 300F 0086           		mov	PortB,#0fh	; Clear PortB

248    00BB- 3004 009A           		mov	cntr_col,#4	; Test four times

249    00BD-                     	:loop4

250    00BD- 20D8                		call	row_scan

251    00BE- 3000 049D           		or	flag_row,#00h	; Test flag

252    00C0- 1D03 28CC           		jnz	:finish		; Yes, key press is sensed

253

254    00C2- 039A                		dec	cntr_col

255    00C3- 1903 28C9           		jz	:skip		; Avoid RA4(LED) to be Low

256

257    00C5- 1403                		setb	c		; Column scan

258    00C6- 0D85                		rl	PortA

259    00C7- 0A97                		inc	key_column

260

261    00C8- 28BD                		goto	:loop4

262    00C9-                     	:skip

263    00C9- 30FF 0098           		mov	key_matrix,#no_key

264    00CB- 28D7                		goto	:no_key		; No key is pressed

265

266    00CC-                     	:finish

267    00CC- 0816 0098           		mov	key_matrix,key_row

268    00CE- 3007 0597           		and	key_column,#0000111b	; Use last 3 bits

269    00D0- 1003                		clrb	c

270    00D1- 0D97                		rl	key_column	; Move to upward

271    00D2- 0D97                		rl	key_column

272    00D3- 0817 0798           		add	key_matrix,key_column

273    00D5- 081C 0798           		add	key_matrix,shift_32	; Add 32 in shift mode

274    00D7-                     	:no_key

275    00D7- 0008                		ret

276                              	;---------------

277    00D8-                     	row_scan

278    00D8- 019D                		clr	flag_row

279    00D9- 0196                		clr	key_row

280    00DA- 1E06 28E7           		jnb	col0,:finish

281    00DC- 0A96                		inc	key_row

282    00DD- 1E86 28E7           		jnb	col1,:finish

283    00DF- 0A96                		inc	key_row

284    00E0- 1F06 28E7           		jnb	col2,:finish

285    00E2- 0A96                		inc	key_row

286    00E3- 1F86 28E7           		jnb	col3,:finish

287    00E5- 0A96                		inc	key_row

288    00E6-                     	:exit

289    00E6- 0008                		ret

290

291    00E7-                     	:finish

292    00E7- 0A9D                		inc	flag_row

293    00E8- 28E6                		goto	:exit

294

295                              	;-------------------------

296                              	; TRANSMIT DATA

297                              	;-------------------------

298    00E9-                     	tx_data

299    00E9- 20FE                		call	tx_leader		; 9.0msec leader burst

300

301    00EA- 2130                		call	tx_bit1			; 4.5msec space (gap)

302    00EB- 2130                		call	tx_bit1

303    00EC- 2130                		call	tx_bit1

304

305    00ED- 3049 0093           		mov	tx_data_buff,#code_system	; Send system code

306    00EF- 211C                		call	tx_byte

307

308    00F0- 3049 0093           		mov	tx_data_buff,#code_system

309    00F2- 30FF 0693           		xor	tx_data_buff,#0ffh	; Invert system code

310    00F4- 211C                		call	tx_byte

311

312    00F5- 0814 0093           		mov	tx_data_buff,code_buff	; Send Data code

313    00F7- 211C                		call	tx_byte

314

315    00F8- 0814 0093           		mov	tx_data_buff,code_buff

316    00FA- 30FF 0693           		xor	tx_data_buff,#0ffh	; Invert data code

317    00FC- 211C                		call	tx_byte

318

319    00FD- 2138                		call	tx_bit			; End bit

320

321                              	;--------------------------

322                              	; TRANSMIT LEADER

323                              	;--------------------------

324    00FE-                     	tx_leader			; Send 0 for 9.0msec

325    00FE- 30FF 008C           		mov	time_cntr,#0ffh	; Count 1

326    0100- 2105                		call	:loop

327    0101- 305F 008C           		mov	time_cntr,#time_start	; Additional count

328    0103- 2105                		call	:loop

329

330    0104- 0008                		ret

331

332    0105-                     	:loop

333    0105- 1205                		clrb	led_out		; Turn on LED

334    0106- 0000                		nop

335    0107- 0000                		nop

336    0108- 0000                		nop

337    0109- 0000                		nop

338    010A- 0000                		nop

339    010B- 0000                		nop

340    010C- 1605                		setb	led_out		; Turn off LED

341    010D- 0000                		nop

342    010E- 0000                		nop

343    010F- 0000                		nop

344    0110- 0000                		nop

345    0111- 0000                		nop

346    0112- 0000                		nop

347    0113- 0000                		nop

348    0114- 0000                		nop

349    0115- 0000                		nop

350    0116- 0000                		nop

351    0117- 0000                		nop

352    0118- 038C                		dec	time_cntr	; Count cycles

353    0119- 1D03 2905           		jnz	:loop

354

355    011B- 0008                		ret

356

357                              	;--------------------------

358                              	; TRANSMIT BYTE

359                              	;--------------------------

360    011C-                     	tx_byte				; TX data in tx_data

361    011C- 3008 0095           		mov	bit_cntr,#bit_cnt	; 8bits

362    011E- 1003                		clc

363    011F-                     	:loop

364    011F- 2138                		call	tx_bit		; Transmit LED pulse

365    0120- 0C93                		rr	tx_data_buff	; Adjust duration

366    0121- 1C03 2925           		jnc	:skip0		; Skip if 0

367    0123- 2130                		call	tx_bit1		; Bit 1

368    0124- 2926                		jmp	:finish

369    0125-                     	:skip0

370    0125- 212A                		call	tx_bit0		; Bit 0

371    0126-                     	:finish

372    0126- 0395                		dec	bit_cntr

373    0127- 1D03 291F           		jnz	:loop

374

375    0129- 0008                		ret

376

377                              	;-------------------------

378                              	; BIT 0 DURATION

379                              	;-------------------------

380    012A-                     	tx_bit0

381    012A- 3078 008C           		mov	time_cntr,#time_0

382    012C-                     	:loop

383    012C- 038C                		dec	time_cntr

384    012D- 1D03 292C           		jnz	:loop

385

386    012F- 0008                		ret

387

388                              	;-------------------------

389                              	; BIT 1 DURATION

390                              	;-------------------------

391    0130-                     	tx_bit1

392    0130- 30FA 008C           		mov	time_cntr,#time_1

393    0132-                     	:loop

394    0132- 038C                		dec	time_cntr

395    0133- 0000                		nop

396    0134- 0000                		nop

397    0135- 1D03 2932           		jnz	:loop

398

399    0137- 0008                		ret

400

401                              	;--------------------------

402                              	; TRANSMIT LED PULSE

403                              	;--------------------------

404    0138-                     	tx_bit

405    0138- 3016 008C           		mov	time_cntr,#time_h

406    013A-                     	:loop

407    013A- 1205                		clrb	led_out		; Turn on LED

408    013B- 0000                		nop

409    013C- 0000                		nop

410    013D- 0000                		nop

411    013E- 0000                		nop

412    013F- 0000                		nop

413    0140- 0000                		nop

414    0141- 1605                		setb	led_out		; Turn off LED

415    0142- 0000                		nop

416    0143- 0000                		nop

417    0144- 0000                		nop

418    0145- 0000                		nop

419    0146- 0000                		nop

420    0147- 0000                		nop

421    0148- 0000                		nop

422    0149- 0000                		nop

423    014A- 0000                		nop

424    014B- 0000                		nop

425    014C- 0000                		nop

426    014D- 038C                		dec	time_cntr	; Count cycles

427    014E- 1D03 293A           		jnz	:loop

428

429    0150- 0008                		ret

430

431                              	;--------------------------

432                              	; DELAY ROUTINES

433                              	; (Multi entry Multi exit)

434                              	;--------------------------

435    0151-                     	delay_1sec

436    0151- 300A 0091           		mov	cntr_1sec,#10

437    0153-                     	:loop

438    0153- 215C                		call	delay_100msec

439    0154- 0B91 2953           		djnz	cntr_1sec,:loop

440

441    0156- 0008                		ret

442

443                              	;------------

444    0157-                     	delay_nmsec

445    0157- 0092                		mov	cntr_nmsec,w	; Delay W msec

446    0158-                     	:loop

447    0158- 2169                		call	delay_1msec

448    0159- 0B92 2958           		djnz	cntr_nmsec,:loop

449

450    015B- 0008                		ret

451                              	;------------

452    015C-                     	delay_100msec

453    015C- 3064 0090           		mov	cntr_100msec,#100

454    015E-                     	:loop

455    015E- 2169                		call	delay_1msec

456    015F- 0B90 295E           		djnz	cntr_100msec,:loop

457

458    0161- 0008                		ret

459                              	;------------

460    0162-                     	delay_15msec

461    0162- 300F 008F           		mov	cntr_15msec,#15

462    0164-                     	:loop

463    0164- 2169                		call	delay_1msec

464    0165- 0B8F 2964           		djnz	cntr_15msec,:loop

465

466    0167- 0008                		ret

467                              	;------------

468    0168-                     	delay_2msec

469    0168- 2169                		call	delay_1msec

470                              	;------------

471    0169-                     	delay_1msec

472    0169- 3080 008E           		mov	cntr_1msec,#80h	; 1msec delay for 3.58MHz

473    016B-                     	:loop

474    016B- 0000                		nop

475    016C- 0000                		nop

476    016D- 0000                		nop

477    016E- 0000                		nop

478    016F- 0B8E 296B           		djnz	cntr_1msec,:loop

479

480    0171- 0008                		ret

481

482

===== Errors: 0 =====